Customer Service Department  Fast Fax

To:	FAROArm User		From:	Customer Service Department

Form: 178-111

4 Pages total including this page.  Contact us immediately if pages are missing or not legible.

# TOPIC: TROUBLESHOOTING Cable Pin Outs

* Important: PLEASE READ BEFORE BEGINNING THE PROCESS *

This document is design to give the customer the ability to inspect and diagnose cables when experiencing problems such as communication errors, error codes, & intermittent operation.

AC031 FARO Arm Power Cable (1456)

This cable is used with several different types of FARO Arms: (Silver Series, Gold Series, Sterling Series & Bronze Millennium Series.)

Using a fluke you can pin out the AC031 cable to check for intermittent problems.  If a problem is discovered do not attempt to repair the cable contact the FARO Technologies’ customer service department for replacement.

Pin Out Information (Pin for Pin)

Pin 1 - Ground

Pin 2 - R1 In

Pin 3 - T1 Out

Pin 4 - RTS

Pin 5 - Ground

Pin 6 - 12V Ana

Pin 7 - 12V Ana

## XH16-0237 6’ Serial Communication Cable

This cable is used with a FARO Arm: (Bronze Series Only)

Using a fluke you can pin out the XH16-0237 cable to check for intermittent problems.  If a problem is discovered do not attempt to repair the cable contact the FARO Technologies’ customer service department for replacement.

I2-09 (AC029) Serial Cable (Silver Series Arms Only)

Using a fluke you can pin out the AC029 cable to check for intermittent problems.  If a problem is discovered do not attempt to repair the cable contact the FARO Technologies’ customer service department for replacement.

## AC032 10’ Null Modem Communication Cable

This cable is used with several different types of FARO Arms: (Silver Series, Gold Series, Sterling Series & Bronze Millennium Series.)

Using a fluke you can pin out the AC032 cable to check for intermittent problems.  If a problem is discovered do not attempt to repair the cable, contact FARO Technologies’ customer service department for replacement.

## XH11-0118 25’ RJ 11 Cable

This cable is used with some Bronze & Space Arms.

Using a fluke you can pin out the XH11-0118 cable to check for intermittent problems.  If a problem is discovered do not attempt to repair the cable, contact FARO Technologies’ customer service department for replacement.

## 2491 Control Station 20 Cable

This cable is used with IBM Netvista Computers and Gold arms only.

Using a fluke you can pin out the 2491 cable to check for intermittent problems.  If a problem is discovered do not attempt to repair the cable, contact FARO Technologies’ customer service department for replacement.

If you are still experiencing difficulties, please contact the customer service department by telephone at 1-800-736-2771 or by e-mail at support@FARO.com.

PLEASE FAX YOUR QUESTIONS TO (407) 333.8056

# Text boxes

B

B

R

R

G

G

Y

Y