|  | Application Method Sheet Accessories: Wireless Remote for the Faro Laser Tracker |
| --- | --- |
| Programming Wireless Remote for use with CAM2 Measure Application Description We will be programming the buttons 1-4 on the top of the Laser Tracker Remote. You need to make sure that you have installed the software (on the CD that came in the box with the remote control). Setup Once the software has been installed on your computer you will see a RF symbol in the lower right side of your screen in the task bar. If you are using Windows XP you may need to expand your menu by clicking on the double left pointing arrows to the left of the task bar. Double left mouse click on the RF symbol. The screen titled RemotePoint RF – presentation will appear like you see in Figure 1. Now we will change the settings on the buttons to match the functions we want each button to do. I suggest Button 1=P, which stands for Probe. This allows you to changes probes as you measure (i.e. different size SMR’s, pin nests, etc). I suggest Button 2=T, which stands for Tracker. This allows you to Reset the Interferometer Laser, in other words it send the tracker beam back to the Home position (or any reset point you have previously setup). I suggest Button 3=Insert, which stands for Measure. This allows you to take measurements. It also allows you to accept your measurement Results without moving the mouse to the OK button. I suggest Button 4=Home, which stands for Compensation. This allows you to compensate you measurements. It also allows you to cancel your measurement Results without moving the mouse to the Cancel button. To program each button you need to right mouse click on the button and go to the Replace Tool>General>Keystroke. Go to the Pull Down Menu and select keystroke you want, see my suggestions above. Then click OK and continue with the same steps on the next remote button. Once you have the buttons setup the way you want we will need to save the settings. Go to File>Save as you see in Figure 4. You can now close this window by either going to File>Exit or click on the little x in the upper right corner of the window. Congratulations your remote is now setup to use with your Faro Laser Tracker and CAM2 software. Good Measuring! |  |
| USA: Orlando, Detroit, Los Angeles, Chicago, Charlotte, Columbus, Seattle Europe: Paris, France; Stuttgart, Gernany; Coventry, UK;Barcelona, Spain; Rivoli, Italy Asia: Aichi, Japan 407.324.7876 Fax: 407.333.4181 E-Mail: info@faro.com www.faro.com |

# Text boxes

# Figure 1

# Figure 2

# Figure 3

# Figure 4