| Product Specification |
| --- |
| Part Number: 11516 |
| Issue Date: 01/04/2008 |
| Revision: 0 | By: R. Sanville |
| Rev. Date: 01/04/2008 | Page: 1 of 1 |

- Description:

This is a magnetic mount kit that allows any FaroArm, Gage or Laser Tracker to be mounted to surface plates, tool beds and other ferrous surfaces.  The part number consists of the following:

(1) 150.0 mm diameter magmount, (1) hex wrench, (1) test certificate, (1) operating manual.

- Physical:

| Overall Diameter: | 150.0 mm (5.905”) |
| --- | --- |
| Face Diameter: | 136.5 mm (5.375”) |
| Overall Height: | 57.3 mm (2.257”) |
| Weight: | 7.50 Kg. (16.5 lbs.) reference |
| Finish: | 63 RMS |
| Flatness: | .018 mm (0.0007”) maximum |

- Performance/Operation:

FARO part number 1149 is attached to the base allowing FARO Arms and Gages to be threaded onto the magmount.

| Deflection of floating 12’ Arm during use: | 7 microns (.00028”) (reference) |
| --- | --- |
| Deflection of 12’ Arm pushed down (45 degree angle relative to base) during use: | 9 microns (.00035”) (reference) |
| Torque required to turn on and off: | 6.77 N*M (5 Ft*lbs.) maximum |
| Full surface contact breakaway force: | 453.6 Kg. (1000 lbs.) |
| Sliding breakaway force: | 90.7 Kg. (200 lbs.) |
| Sealing: | Internal o-ring |
| Corrosion Protection: | Packed in plastic bag with desiccant, rust protection fluid applied to surface prior to shipment. |
| Operating Temperature | 0-65.6°C (32-150°F) |

- Packaging:

The product is packaged in a cardboard box with (1) set of foam packaging inserts.