Customer Service Department Fast Fax

To: FARO  User		From:  Customer Service Department

1 Page total including this page.  Contact us immediately if pages are missing or not legible.

Tips to Maximize a Move Device Position

Often times, a move device position (or leap frog) is needed when measuring an article that is bigger than the actual span of the measuring device.  Here are some tips to make sure that an efficient move device command is made every time.

Space out your points.  A Move Device Position relies on triangulation.  When running a move device, make sure a wide area is being covered relative to the distance the arm is moving, i.e. if the arm is moving a span of  8 feet, you want to make sure that the points cover an area of more than 5 in2.

Make sure the locations of the reference points are 3 dimensional.  If you use only 3 reference points, try to stray away from the habit of placing them on the same 2D plane or surface, especially if the locations are symmetrical to each other as this may confuse the computer’s calculations.

Use more than 3 reference points.  It never hurts to have too much data so try to use as many reference points as possible.  The outcome may result in a tighter fit.

Recalculate for a better fit.  If the above 3 methods haven’t worked, filter out the worst points after running the command and recalculate.  This’ll ensure a more accurate fit.

If you are still experiencing difficulties, please contact the customer service department by telephone at 1-800-736-2771 or by e-mail at support@FARO.com.   FAX questions to:  (407) 333-8056