Customer Service Department Technical Guides

Topic: How to install & program Remote Point Presenter Remote for FARO Laser Tracker

7 Pages total including this page. Contact FARO’s CSD Department immediately if pages are missing or not legible.

# Note the system requirement for installation: Windows 98, ME, 2000 or XP, Available USB port, 6MB of available hard disk space

# IMPORTANT NOTE:  These instructions apply only to the VP4300 RemotePoint Presenter from Interlink Electronics.  This model has been discontinued by Interlink Electronics and was replaced with the VP4350 Remote Point Presenter.  The physical appearance of these two remotes is identical but there are minor differences in the appearance of the USB portion that connects into the computer where model number can be found.  According to information on Interlinks web site, the newer VP4350 does not have software to perform custom programming for use with the FARO Laser Tracker.

# 1) Insert the RemotePoint Presenter CD into the CD Rom drive, install the program.

# 2) Go to START>ALL PROGRAMS>INTERLINK ELECTRONICS>REMOTEPOINT PRESENTER>REMOTEPOINT PRESENTER

# You will see the following picture:

# 3) Right click on your preferred programming button, you will see following.

# 4) Uncheck shift and control, pull down tab to select “insert”

# 5) Perform steps 1 to 4 on other prefer button.

# 6) Click “Ok” then save as a profile

# 7) Key in a profile name and Click “save”

# 8) Go to File > Close and you may start to use the remote controller, but remember prior to use, you need to plug-in the remote receiver into any USB port.  The slowly flashing green light means that the receiver is working after you have plugged in.  The RemotePoint Presenter Remote share a unique address with the receiver, you should not re-program it unless you have trouble with the communication between the RemotePoint Presenter Remote and the receiver.

# For first time use only

# On the remote point presenter remote, press the laser button and shine the laser beam on the receiver’s starburst icon for about 5 seconds, when the green light glows steadily the receiver is programmed to the unique address of the Remote Point Presenter remote.  After address is established, the LED will return to blinking green.

# The Remote Controller is ready to use.

# Revision History

| For questions and concerns please email FARO Customer Service: |
| --- |
| FARO Technologies Inc. 250 Technology Park Lake Mary, FL 32746 1-800-736-2771 support@FARO.com | FARO Europe Lingwiesenstraße 11/2 70825 Korntal-Münchingen, Germany +49 7150 9797-400 support@FAROeurope.com | FARO Singapore No. 3 Changi South Street 2 #01-01 Xilin Districentre Building B Singapore 486548 65 6511 1350 supportAP@FARO.com |
| Disclaimer: FARO Technologies, Inc. makes no warranty, express, implied or statutory, as to the material on this form, including any referenced third party. The material contained on this form is for informational purposes only; such material is provided “AS IS” and with all faults, and your use of the material is at your own risk. |